## Slide 1
PART 9
IPv6

## Slide 2
Part 01
1 - 1. IPv6 주소 표기법
. IPv4와 IPv6 주소 표기 방식 비교
8bit | 8bit | 8bit | 8bit
11111111 | 11111111 | 11111111 | 11111111
16bit | 16bit | 16bit | 16bit | 16bit | 16bit | 16bit | 16bit
FFFF | FFFF | FFFF | FFFF | FFFF | FFFF | FFFF | FFFF
FDEC | AB98 | 0065 | 3210 | 000C | ACDE | 0000 | FFFF
FDEC | AB98 | 65 | 3210 | C | ACDE | 0 | FFFF
1) 규칙 : IPv6의 “ 0 “ 값을 포함하는 주소에 대한 주소 생략 방법 : 각 필드의 최상위 0일 경우 또는 연속적인 0일 경우 생략법
2) 규칙 : IPv6의 “ 0 “ 값을 포함하는 주소에 대한 주소 생략 방법 : 각 필드에 연속적인 0을 한 번 이상 생략 불가
(연속된 0의 필드를 생략 후 콜론(::)으로 표기)
BEFF | AB98 | 0 | 0 | 0 | ACDE | 0 | FFFF
BEFF | AB98 | :: | ACDE | 0 | FFFF
F = 1111 (8421)
마디당 8비트 , 10진수로 표현

## Slide 3
Part 01
1 - 2. IPv6 주소 요약 표현 문제
IPv6 주소 : 2001:0DA7:0001:BAC1:0000:0000:A123:FFFF
요약 :
2) IPv6 주소 : FE80:0000:0000:0000:0321:5FFF:CAFE:FE7E
요약 :
3) IPv6 주소 : FF02:0000:0000:0000:0000:0000:0000:0001
요약 :
4) IPv6 주소 : FF03:0000:0000:0000:5FCD:0000:0000:0123
요약 :
5) IPv6 주소 : AC78:2000:4000:3000:0000:0000:0000:46CD
요약 :
6) IPv6 주소 : 3213:0005:0006:0007:0008:0000:54DF:0001
요약 :
7) IPv6 주소 : FF02:7401:0000:0000:4CAC:0000:0000:0001
요약 :
8) IPv6 주소 : 2001:DB80:0001:0000:0000:0000:0000:0001
요약 :
9) IPv6 주소 : FF02:0000:0000:0000:0000:0000:0000:0001
요약 :

## Slide 4
Part 01
1 - 2. IPv6 주소 요약 표현 답
IPv6 주소 : 2001:0DA7:0001:BAC1:0000:0000:A123:FFFF
요약 : 2001:DA7:1:BAC1::A123:FFFF
2) IPv6 주소 : FE80:0000:0000:0000:0321:5FFF:CAFE:FE7E
요약 : FE80::321:5FFF:CAFE:FE7E:CC7D
3) IPv6 주소 : FF02:0000:0000:0000:0000:0000:0000:0000:0001
요약 : FF02::1
4) IPv6 주소 : FF03:0000:0000:0000:5FCD:0000:0000:0123
요약 : FF03:0:0:0:5FCD::123
5) IPv6 주소 : AC78:2000:4000:3000:0000:0000:0000:46CD
요약 : AC78:2000:4000:3000::46CD
6) IPv6 주소 : 3213:0005:0006:0007:0008:0000:54DF:0001
요약 : 3213:5:6:7:8::54DF:1
7) IPv6 주소 : FF02:7401:0000:0000:4CAC:0000:0000:0001
요약 : FF02:7401::4CAC:0:0:1
8) IPv6 주소 : 2001:DB80:0001:0000:0000:0000:0000:0001
요약 : 2001:DB80:1::1
9) IPv6 주소 : FF02:0000:0000:0000:0000:0000:0000:0001
요약 : FF02::1

## Slide 5
Part 01
1 - 3. IPv6 Network 와 Host ID 구분
16bit | 16bit | 16bit | 16bit | 16bit | 16bit | 16bit | 16bit
FFFF | FFFF | FFFF | FFFF | FFFF | FFFF | FFFF | FFFF
Network 구간 (60 bits) | Host 구간 (68 bits)
2001:0DB7:0000:CA3 | 0:0000:0000:0000:0000
1) Network ID와 Host ID 구간
8 4 2 1 = 4bit
2001:0DB7:0000:CA30:0000:0000:0000:0000/60
2001:DB7:0:CA30::/60
문제) 위의 네트워크 대역에서 가질 수 있는 Host 주소의 범위는 ?
2001:DB7:0:CA30:: ~ 2001:DB7:0:CA3F:FFFF:FFFF:FFFF:FFFF

## Slide 6
Part 01
2 - 1. IPv6 주소 종류
. Broadcast 방식을 없애고, Anycast 방식을 채택
IPv4 | IPv6
Unicast | Unicast
Multicast | Multicast
Broadcast | Anycast
: Anycast 주소를 목적지로 하는 패킷을 가장 가까운 노드로 전달하는 방식

## Slide 7
Part 01
2 - 2. IPv6 주소 종류
. IPv6 유니캐스트 주소 종류
IPv4 | IPv6
Unicast | Unicast
Multicast | Multicast
Broadcast | Anycast
Unicast Address | Global Unicast Address
 | Link-Local Unicast Address
 | Unique Local Unicast Address
 | 기타 Address
Multicast Address | 
Anycast Address | 

## Slide 8
Part 01
2 - 3. IPv6 주소의 공통적 특징
. IPv6의 인터페이스는 복수의 Unicast, Multicast, Anycast 주소를 가질 수 있음.
- Scope
Global
Scope
(전세계)
Site-Local
Scope
(학교, 회사 등)
없어짐
Link-Local Scope
(Intra-Network)
IPv6 Prefix | Allocation | Reference
2000::/3 | Global Unicast | RFC4291
FC00::/7 | Unique Local Unicast | RFC4293
FE80::/10 | Link-Local Unicast | RFC4291
FF00::/8 | Multicast | RFC4291
http://www.ietf.org/rfc.html

## Slide 9
Part 01
3. Global Unicast Address
. 글로벌 유니캐스트 주소
- MSB (Most Significant Byte) 3Bit는 무조건 “001”로 시작
“2XXX:” 또는 “3XXX:”로 시작하면 무조건 Unicast Address : 2000::/3(0010 0000 0000 0000) ~ 3FFF:: /3(0011 1111 1111 1111)
- IANA(Internet Assigned Numbers Authority)는 “2000::/3”의 Global Unicast Address를 보유하고 APNIC에게 “2001:200:: /23”을 할당
└ APNIC는 KRNIC -> 한국인터넷진흥원(KISA)에게 “2001:290::/32”를 할당하고 KISA가 SK 브로드밴드에게 할당
- SK 브로드밴드는 “2001:290:XXXX:XXXX::/48”로 지역별 설계
└ SK 브로드밴드의 인터넷을 사용하는 기관 등은 “2001:290:XXXX:XXXX::/48” 주소를 할당 받음.
APNIC | 23bits | 
KISA | 32bits | 
SK Broadband | 48bits | 
Customer | 48bits | 16bits | 
IANA | 3bits | 
 | 001 | 
IPv6 주소 체계 | Network 구간 (64 bits) | Host 구간 (64 bits)

## Slide 10
Part 01
4. IPv4 및 IPv6 주소 체계 대응 관계
구분 | IPv5 주소 | IPv6 주소
멀티캐스트 주소 | 224.0.0.0/4 (D Class) | FF00::/8
브로드캐스트 주소 | 255.255.255.255 | 없음  애니캐스트
미지정 주소 | 0.0.0.0/32 | ::/128
루프백 주소 | 127.0.0.1 | ::1/128
공인 IP 주소 | 공인 IP 주소 | Global Unicast Address
사설 IP 주소 | 10.0.0.0/8 172.16.0.0/12 192.168.0.0/16 | FC00::/7  Unique local
링크 로컬 주소 | 169.254.0.0/16 | FE80::/64  Link-local
※ IPv4 및 IPv6 주소 체계 대응 관계

## Slide 11
Part 01
5. Link-Local Unicast Address
. ipv6 address 2001:290:1:1::1/64 : 자신이 IP 주소를 할당
. ipv6 address 2001:290:1:1::/64 eui-64 : Interface ID가 자동으로 설정
[ EUI-64 Format 생성 절차 ]
장비의 인터페이스에 IPv6가 활성화되거나 또는 인터페이스에 글로벌 주소를 부여하면
해당 주소가 부여되기 전에 먼저 EUI-64 (Extended Unique Identifier-64)라고 하는 포맷으로 주소가 자동으로 부여된다.
MAC 주소 48bit |  | 
000A | B73D | 21E0
0000 00*0 0000 1010
최상위 일곱번째 비트가 0이면 1로 변환
최상위 일곱번째 비트가 1이면 0으로 변환
MAC 주소 48bit |  | 
000A | B7 3D | 21E0
Interface ID 64bit |  |  | 
000A | B7FF | FE3D | 21E0
EUI-64 Format 64bit
Network ID 64bit
FE80::
ipv6 address 2001:290:1:1::/64 eui-64 ??

## Slide 12
Part 01
6. IPv6 Routing Protocol – Static 1
R1
R2
2002::1/64
2002::2/64
# show ipv6 int brief
# show ipv6 route
# show ipv6 int s0/0
s0/0
s0/0
fa0/0
2003::2/64
fa0/0
2004::2/64
2003::1/64
2004::1/64
ipv6 unicast-routing
interface s0/0
ipv6 address 2002::1/64
no shutdown
interface f0/0
ipv6 address 2003::2/64
no shutdown
ipv6 unicast-routing
interface s0/0
ipv6 address 2002::2/64
no shutdown
interface fa0/0
ipv6 address 2004::2/64
no shutdown
ipv6 route 2004::/64 2002::2
ipv6 route 2003::/64 2002::1
Notes: 2811 라우터

## Slide 13
Part 01
7. IPv6 Routing Protocol – Static 2
R1
R2
2002::1/64
2002::2/64
# show ipv6 int brief
# show ipv6 route
# show ipv6 int s0/0
s0/0
s0/0
fa0/0
2003::2/64
fa0/0
2004::2/64
2003::1/64
2004::1/64
ipv6 unicast-routing
interface s0/0
ipv6 address 2002::1/64
no shutdown
interface f0/0
ipv6 address 2003::2/64
no shutdown
ipv6 unicast-routing
interface s0/0
ipv6 address 2002::2/64
no shutdown
interface fa0/0
ipv6 address 2004::2/64
no shutdown
ipv6 route 2004::/64 s0/0 “이웃 링크 로컬 주소”
ipv6 route 2003::/64 s0/0 “이웃 링크 로컬 주소”
Notes: 2811 라우터

## Slide 14
Part 01
8. IPv6 Routing Protocol – Default
R1
R2
2002::1/64
2002::2/64
# show ipv6 int brief
# show ipv6 route
# show ipv6 int s0/0
s0/0
s0/0
fa0/0
2003::2/64
fa0/0
2004::2/64
2003::1/64
2004::1/64
ipv6 unicast-routing
interface s0/0
ipv6 address 2002::1/64
no shutdown
interface f0/0
ipv6 address 2003::2/64
no shutdown
ipv6 unicast-routing
interface s0/0
ipv6 address 2002::2/64
no shutdown
interface fa0/0
ipv6 address 2004::2/64
no shutdown
ipv6 route 0::/0 2002::2
ipv6 route 0::/0 2002::1
Notes: 2811 라우터

## Slide 15
Part 01
9. IPv6 Routing Protocol – Static 4
R1
R2
2002::/64 EUI-64
2002::2/64 EUI-64
# show ipv6 int brief
# show ipv6 route
# show ipv6 int s0/0
s0/0
s0/0
fa0/0
2003::/64 EUI-64
fa0/0
2004::/64 EUI-64
2003::1/64
2004::1/64
ipv6 unicast-routing
interface s0/0
ipv6 address 2002::/64 EUI-64
no shutdown
interface f0/0
ipv6 address 2003::/64 EUI-64
no shutdown
ipv6 unicast-routing
interface s0/0
ipv6 address 2002::/64 EUI-64
no shutdown
interface fa0/0
ipv6 address 2004::/64 EUI-64
no shutdown
ipv6 route 0::/0 2002:확인
ipv6 route 0::/0 2002:확인
Default Gateway : 확인
Default Gateway : 확인
Notes: 2811 라우터

## Slide 16
Part 01
10. IPv6 Routing Protocol – autoconfig
R2
# show ipv6 int brief
# show ipv6 route
# show ipv6 int s0/0
f0/1
2002::2/64
fa0/0
2003::2/64
R1
2003::1/64
ip auto
ip auto
라우터일 경우 : ipv6 address autoconfig
Notes: 2811 라우터

## Slide 17
Part 01
11. IPv6 Routing Protocol – RIPng
R1
R2
2002::1/64
2002::2/64
# show ipv6 int brief
# show ipv6 route
# show ipv6 int s0/0
s0/0
s0/0
fa0/0
2003::2/64
fa0/0
2004::2/64
2003::1/64
2004::1/64
ipv6 unicast-routing
ipv6 router rip 100
interface s0/0
ipv6 address 2002::1/64
ipv6 rip 100 enable
no shutdown
interface f0/0
ipv6 address 2003::2/64
ipv6 rip 100 enable
no shutdown
ipv6 unicast-routing
ipv6 router rip 100
interface s0/0
ipv6 address 2002::2/64
ipv6 rip 100 enable
no shutdown
interface fa0/0
ipv6 address 2004::2/64
ipv6 rip 100 enable
no shutdown
RIPng : Next-Generation
Multicast (Hello Packet)
RIPv2 : 224.0.0.9
RIPng : FF02::9
Notes: 2811 라우터

## Slide 18
Part 01
12. IPv6 Routing Protocol – EIGRP
R1
R2
2002::1/64
2002::2/64
# show ipv6 int brief
# show ipv6 route
# show ipv6 int s0/0
s0/0
s0/0
fa0/0
2003::2/64
fa0/0
2004::2/64
2003::1/64
2004::1/64
ipv6 unicast-routing
ipv6 router eigrp 100
eigrp router-id 1.1.1.1
no shutdown
interface s0/0
ipv6 address 2002::1/64
ipv6 eigrp 100
no shutdown
interface f0/0
ipv6 address 2003::2/64
ipv6 eigrp 100
no shutdown
ipv6 unicast-routing
ipv6 router eigrp 100
eigrp router-id 1.1.2.2
no shutdown
interface s0/0
ipv6 address 2002::2/64
ipv6 eigrp 100
no shutdown
interface fa0/0
ipv6 address 2004::2/64
ipv6 eigrp 100
no shutdown
EIGRP 100
Multicast (Hello Packet)
EIGRP : 224.0.0.10
EIGRP : FF02::10
Notes: 2811 라우터

## Slide 19
Part 01
13. IPv6 Routing Protocol – OSPF
R1
R2
2002::1/64
2002::2/64
# show ipv6 int brief
# show ipv6 route
# show ipv6 int s0/0
s0/0
s0/0
fa0/0
2003::2/64
fa0/0
2004::2/64
2003::1/64
2004::1/64
ipv6 unicast-routing
ipv6 router ospf 1
router-id 1.1.1.1
interface s0/0
ipv6 address 2002::1/64
ipv6 ospf 1 area 0
no shutdown
interface f0/0
ipv6 address 2003::2/64
ipv6 ospf 1 area 0
no shutdown
ipv6 unicast-routing
ipv6 router ospf 1
router-id 1.1.2.2
interface s0/0
ipv6 address 2002::2/64
ipv6 ospf 1 area 0
no shutdown
interface fa0/0
ipv6 address 2004::2/64
ipv6 ospf 1 area 0
no shutdown
OSPF 1 Area 0
Multicast (Hello Packet)
OSPF : 224.0.0.5 - 6
OSPF : FF02::5 - 6
Notes: 2811 라우터